4 Tile example and more
Purpose:
Understand EM_aligner, MATLAB code base for assembling and solving EM-connectomics fine alignment problems.
Understand the linear algebra going into these solutions.
Develop plan for scaling the solver for large chunks of mm2 sections.

---
Source of Data

---
4 Tiles and Point Matches

---
Filtering
EM_aligner includes filtering to limit the number of included point matches.
In this example, the filtering reduced the # from 200 points per tile pair to ~50.

---
Naming
1,2P:
1,2Q:
1x1,1y1
2x1,2y1
1x2,1y2
2x2,2y2
...
...
Tile 1
2,4P:
Tile 2
2x1,2y1
2x2,2y2
2x2,2y2
4,3P
...
2,4Q:
4x1,4y1
4,3Q
4x2,4y2
...
Tile 3
Tile 4
4,3P
4,3Q

---
Affine Transformation
The point match coordinates in each tile will be transformed according to an affine transformation:
The goal of alignment between two tiles is to meet the criteria:
Explicitly:
1u1 = a11x1 + b11y1 + c1
1v1 = d11x1 + e11y1 + f1
1u1 = 2u1
1v1 = 2v1
1u2 = 2u2
1v2 = 2v2
...

---
Matrix Assembly
which is the same as:
And for multiple pairs of points:
Reorder to keep all tile 1 coordinates in a column block

---
Matrix Assembly
Block-wise shorthand:
2 tiles:
3 tiles:
4 tiles:

---
Matrix Assembly (from data)
Force filtering to limit to 10 point matches per tile, for easy visualization:
Non-zero structure
value-colored
1,3P
1,3Q
The ordering is a little different than the example, but, it’s just block-wise row permutations:
3,4P
3,4Q
1,2P
1,2Q
2,4P
2,4Q
We know these values. They are the coordinates of the point matches.
We want to know these transform values, and apply them to the image data.

---
Least Squares
For this simple problem, there are:
80 equations (4 tile matches x 10 points x 2 DOF)
24 unknowns (4 tiles x (2 affine +1 translation) x 2 DOF)
The system is overdetermined.
Use linear least-squares to determine the best possible set of transformations.
Per row (i) residual:
We want norm2 to be as small as possible:

---
Least Squares
Find the minimum by seeking where the gradient relative to the parameters =0
Per row (i) residual:
gradient
We want norm2 to be as small as possible:
gradient, expanded
rearranged
Matrix notation
This product is a square matrix (24x24, in our example).
Now there are 24 equations and 24 unknowns.

---
Weighting and Regularization
Our new matrix equation:
We can weight each row of A differently
Example: within-section point matches should be weighted more than cross-section point matches
We can regularize
Derivation to-be-added, but, it’s much like on the last page, with an additional term in S that increases S if the solution strays far from a first guess/approximation fo x
Renaming things:

---
Properties of K and Lm
Lm has non-zero values
K is symmetric
K is symmetric
Which we can see easily from re-ordering rows and columns:
The graph of K shows two separate sub-matrices.
This type of structure will be important for partitioning large matrices for distributed solving.
I know about 2 partitioning packages for this:
Scotch: used by the Pastix solver. (Also, PT-Scotch for parallel partitioning.)
METIS. Also, (ParMetis)

---
Size estimate for 1mm3
- Estimate for K
  - Ntiles = 2.5e8 = (1e4 tiles/section)x(2.5e4 sections)
  - K m x n = 1.5e9 x 1.5e9 (6DOF per tile)
  - Guess that each tile has point matches to 10 other tiles.
  - nnz = 5e10 (each row has 3*(10+1) nz entries)
- Similar (?), smaller matrix: Janna/Queen_4147 (SuiteSparse...):
  - m x n = 4.1e6 x 4.1e6
  - nnz = 3.2e8

---
First pastix with Janna/Queen_4147
root@15884987838d:/app/pastix_5.2.3/src/example/bin# ./simple -MM /app/matrices/Queen_4147.mtx
MPI_Init_thread level = MPI_THREAD_MULTIPLE
driver: MatrixMarket file: /app/matrices/Queen_4147.mtx
open RHS file : /app/matrices/Queen_4147.mtx.rhs
cannot load /app/matrices/Queen_4147.mtx.rhs
Setting right-hand-side member such as X[i] = i
Check : Numbering	OK
Check : Sort CSC	OK
Check : Duplicates	OK
 +--------------------------------------------------------------------+
 + PaStiX : Parallel Sparse matriX package +
 +--------------------------------------------------------------------+
  Matrix size 4147110 x 4147110
  Number of nonzeros in A 166823197
 +--------------------------------------------------------------------+
 + Options +
 +--------------------------------------------------------------------+
        Version :
        SMP_SOPALIN : Defined
        VERSION MPI : Defined
        PASTIX_DYNSCHED : Not defined
        STATS_SOPALIN : Not defined
        NAPA_SOPALIN : Defined
        TEST_IRECV : Not defined
        TEST_ISEND : Defined
        TAG : Exact Thread
        FORCE_CONSO : Not defined
        RECV_FANIN_OR_BLOCK : Not defined
        OUT_OF_CORE : Not defined
        DISTRIBUTED : Defined
        METIS : Not defined
        WITH_SCOTCH : Defined
        INTEGER TYPE : int
        PASTIX_FLOAT TYPE : double
 +--------------------------------------------------------------------+
   Time to compute ordering 46.2 s
   Time to analyze 5.09 s
   Number of nonzeros in factorized matrix -2147483648
   Fill-in -12.8728
   Number of operations (LLt) 2.69604e+14
   Prediction Time to factorize (AMD 6180 MKL) 3.61e+04 s
   --- Sopalin : Threads are binded ---
First, try simple.c (single-threaded...)
1.7e8 nnz before factorization
-2.1e9 nnz after factorization
(note minus sign, I thought I compiled with 64-bit integers, but, now I need to go check)
At start of factorization, RAM usage went up to 115GB. (from ~5GB)
10 hours predicted time to factorize...
This is a terrible example for single-thread, but, good for parallel

---
Janna/Queen_4147 multi-processor
root@15884987838d:/app/pastix_5.2.3/src/example/bin# ./simple -t 12 -MM /app/matrices/Queen_4147.mtx
MPI_Init_thread level = MPI_THREAD_MULTIPLE
driver: MatrixMarket file: /app/matrices/Queen_4147.mtx
open RHS file : /app/matrices/Queen_4147.mtx.rhs
cannot load /app/matrices/Queen_4147.mtx.rhs
Setting right-hand-side member such as X[i] = i
Check : Numbering	OK
Check : Sort CSC	OK
Check : Duplicates	OK
 +--------------------------------------------------------------------+
 + PaStiX : Parallel Sparse matriX package +
 +--------------------------------------------------------------------+
  Matrix size 4147110 x 4147110
  Number of nonzeros in A 166823197
 +--------------------------------------------------------------------+
 + Options +
 +--------------------------------------------------------------------+
        Version :
        SMP_SOPALIN : Defined
        VERSION MPI : Defined
        PASTIX_DYNSCHED : Not defined
        STATS_SOPALIN : Not defined
        NAPA_SOPALIN : Defined
        TEST_IRECV : Not defined
        TEST_ISEND : Defined
        TAG : Exact Thread
        FORCE_CONSO : Not defined
        RECV_FANIN_OR_BLOCK : Not defined
        OUT_OF_CORE : Not defined
        DISTRIBUTED : Defined
        METIS : Not defined
        WITH_SCOTCH : Defined
        INTEGER TYPE : int
        PASTIX_FLOAT TYPE : double
 +--------------------------------------------------------------------+
   Time to compute ordering 46.1 s
   Time to analyze 5.19 s
   Number of nonzeros in factorized matrix -2147483648
   Fill-in -12.8728
   Number of operations (LLt) 2.69604e+14
   Prediction Time to factorize (AMD 6180 MKL) 3.19e+03 s
   --- Sopalin : Threads are binded ---
    - iteration 1 :
        total iteration time 7.57 s
        error 2.4232e-13
   Static pivoting 149446
   Inertia (NB: with pivoting) 4147110
   Time to factorize 1.32e+04 s
   FLOPS during factorization 19.045 GFLOPS
   Time to solve 7.3 s
   Refinement 1 iterations, norm=2.42e-13
   Time for refinement 7.83 s
Precision : ||ax -b||/||b|| = 2.3221479458594105064e-13
Running on em-131db
12 cores
250GB RAM (used 115GB)
3.7 hours
Using simple.c example from pastix. No fancy options.

---
A and K from a whole section (282 tiles)

---
system_solve_affine_with_constraint
EM_aligner
get_section_ids
load_all_transformations
system_solve_helper_load_point_matches
load_montage_pm
load_cross_section_pm
filter_pm_local
filter_pm_consistency
split_PM_XXX.mat
gen_A_b_row_range
Construct K and Lm
solve_AxB
solve_pastix
system_solve_helper_ingest_into_renderer_database
Inspect diagnostics

---
Do these plots make sense?
Change aspect
A size: 50532x1692
1692 = 282tiles x 6DOF/tile
50532 = average of ~190 point matches per overlap